## Slide 1: Jets and HCal Resolution
Brian Page
08/25/2016

## Slide 2
Introduction
Last time: Looked at average absolute value of shift in jet pT with no hadron calorimeter and calorimeter with several resolutions. Resolution of each hadron was multiplied by random factor uniformly distributed between -1 and 1.
This time: Resolution is now taken as Gaussian with sigma equal to the resolution of hadron with specific energy. Have removed the absolute value from the calculation of delta pT. Added purity plots.
Note: What will be shown is not the final jet resolution as I have not considered the resolution from the Emcal. What I want to show is the difference between no hadron calorimeter and a hadron calorimeter with some resolution

## Slide 3
Definitions
Plot (∆pT / pTtrue) Vs pTtrue and altered pT, (∆pT) Vs pTtrue and altered pT, and purity in altered pT bins
∆pT is the difference between the altered jet and the true jet
To determine the jet resolution with no hadron calorimeter, I sum the 4-vectors of all particles which are not neutral hadrons to form my altered jet
To find the jet resolution with a hadron calorimeter I do the following for each neutral hadron in the jet:
  Resolution = (6% + 50%/√Epart) or (12.9% + 68%/√Epart)
  Shift Size = Random * Epart (Random is random number taken from a Gaussian centered at 0 with sigma = resolution)
  New Particle Energy = Particle Energy + Shift Size (If new E < 0, toss particle)
  Reconstruct particle 4-Vector with New Particle Energy, assume massless so that new particle momentum = new particle energy
  Reconstruct altered jet by summing unaltered charged, electromagnetic, and invisible particle 4-vectors with altered neutral hadron 4-Vector
Everything shown in Lab Frame for Q2 = 10 – 100 GeV2

## Slide 4
∆pT / pTtrue Vs pTtrue
No Hadrons
Smear Hadrons
Shift
RMS
No Hadrons
Smear Hadrons
Shift
RMS
Plots of the change in transverse momentum divided by the true transverse momentum plotted vs the true transverse momentum
EIC Calorimeter: 6% + 50%/√E
Blue = No Neutral Red = Smeared Neutral
sPHENIX Calorimeter: 12.9% + 68%/√E
Notes: Upper left is eic

## Slide 5
∆pT / pTtrue Vs pTalt
Plots of the change in transverse momentum divided by the true transverse momentum plotted vs the altered transverse momentum
EIC Calorimeter: 6% + 50%/√E
No Hadrons
Smear Hadrons
Shift
RMS
No Hadrons
Smear Hadrons
Shift
RMS
Blue = No Neutral Red = Smeared Neutral
sPHENIX Calorimeter: 12.9% + 68%/√E

## Slide 6
No Hadrons
Smear Hadrons
Shift
RMS
No Hadrons
Smear Hadrons
Shift
RMS
∆pT Vs pTtrue
Plots of the change in transverse momentum plotted vs the true transverse momentum
EIC Calorimeter: 6% + 50%/√E
Blue = No Neutral Red = Smeared Neutral
sPHENIX Calorimeter: 12.9% + 68%/√E

## Slide 7
No Hadrons
Smear Hadrons
Shift
RMS
No Hadrons
Smear Hadrons
Shift
RMS
Plots of the change in transverse momentum plotted vs the altered transverse momentum
EIC Calorimeter: 6% + 50%/√E
Blue = No Neutral Red = Smeared Neutral
sPHENIX Calorimeter: 12.9% + 68%/√E
∆pT Vs pTalt

## Slide 8
Purity
Plots of the true jet transverse momentum vs the altered transverse momentum
The purity in each altered transverse momentum bin is also shown
EIC Calorimeter: 6% + 50%/√E
Purity = (Ngen – Nout)/(Ngen – Nout + Nin)
sPHENIX Calorimeter: 12.9% + 68%/√E